## Slide 1: Complying with Chlorine Gas Regulations
Dave McMillan and Steve Vance
Illinois Rural Water Association

## Slide 2: What we have learned in the last year
U.S. EPA Requirements
Illinois Department of Labor / Occupational Safety and Health Administration Requirements
Illinois Emergency Management Agency/Local Emergency Planning Committee Requirements
Illinois EPA Requirements

## Slide 3: Discussion Outline
IEMA / LAPC
IDoL / OSHA
U.S. EPA
Public awareness
Worker safety concerns
Potential receptors
Quantity doesn’t matter
1,500 pounds
Risk Management
2,500 pounds
Safety procedures and employee training
Reporting Requirements
IL EPA
Permit for use in water treatment
Quantity doesn’t matter
Gas Scrubber

## Slide 4: Compliance with IEMA/LAPC REPORTING REQUIREMENTS
Community Right-To-Know (EPCRA)
Where to report
Compliance

## Slide 5: EPCRA
1986 – Congress passed the Emergency Planning and Community Right-to-Know Act
  Response to Union Carbide releases in Bhopal, India (December 1984) and West Virginia (1985)
  Purpose
    Emergency Planning
    Emergency Release Notification
    Chemical Storage Reporting
    Chemical Release Reporting

## Slide 6: EPCRA NOTIFICATION REQUIREMENTS
Local Planning Requirement Triggered for water supplies
  Chlorine gas is considered an “Extremely Hazardous Substance” with a threshold planning quantity of 100 pounds (Section 302)
  Must notify Local Emergency Planning Committee (LEPC)
  Must notify State Emergency Response Commission (SERC)

## Slide 7: EPCRA LEPC Notification if storing over 100 pounds
Provide name of the water supply Emergency Response Coordinator (ROINC, designee, etc.)
Provide Chlorine Safety Data Sheet (and any other chemicals that are relevant)
Provide additional requested information
Provide changes relevant to emergency planning

## Slide 8: By March 1 every year
Supply Inventory Information to LEPC, the SERC and Local Fire Department
  Use State Specific Tier II Form
    https://iemaohs.illinois.gov/preparedness/serc/serc-tier2.html
      Note: chlorine CAS 7782-50-5

## Slide 9: March 1 Report Continued:
      Note the following excerpt from the url:

## Slide 10: EPCRA Emergency Notification if release more than 10 pounds in 24 hours
Reportable Quantity under EPCRA and the Comprehensive Emergency Response, Compensation, and Liability Act (CERCLA)
  If release more than 10 pounds in 24 hours

## Slide 11: Be prepared to provide details of release immediately (WITHIN 15 MINUTES)
The SERC at 1-800-782-7860 (within state) or (217) 782-7860
The LEPC (for contact information see: https://iemaohs.illinois.gov/content/dam/soi/en/web/iemaohs/preparedness/serc/documents/lepc-releasereportingcontactlist.pdf )
The National Response Center (NRC) at NRC 1-800-424-8802

## Slide 12: EPCRA Release - Immediate Information
Chemical Name
State chlorine gas is an extremely hazardous substance
Estimate quantity lost
Time of release and duration
Where it went (air, land or water)
Health risks and medical concerns (MSDS sheet information)
Community precautions or actions taken (e.g., evacuation, shelter in place, etc.)
Contact Person and phone number

## Slide 13: EPCRA Report - Follow-up Information
Written report (WITHIN 30 DAYS):
  Update initial information
  Actions taken
  Known or anticipated chronic health risks
  Medical attention advice for those exposed

## Slide 14: OSHA WORKER SAFETY
Illinois has an approved State Plan that covers state and local government workers only.
The Division of Occupational Safety and Health (IL OSHA) is part of the Illinois Department of Labor (IDOL). IL OSHA has offices in Springfield, Chicago, and Marion.
Illinois Department of Labor, Division of Occupational Safety and Health Lincoln Tower Plaza 524 South 2nd Street, Suite 400 Springfield, IL 62701 Tel: (217) 782-9386
General Provisions Apply to all Public Works Departments
Water systems that store 1,500 pounds or more chlorine gas.
  Process Safety Management (PSM) Program

## Slide 15: All Public Works Departments
Injury Illness Records
  Recordkeeping - Recordkeeping Forms | Occupational Safety and Health Administration (osha.gov)
Occupational Noise Exposure – Hearing Conservation Program
  Occupational Noise Exposure - Hearing Conservation Program | Occupational Safety and Health Administration (osha.gov)
Exposure to Air Contaminants – Sawing concrete / blacktop, list of hazardous chemicals (Safety Data Sheets)
  OSHA: Protecting Workers From Workplace Air Contaminants (stpub.com)

## Slide 16: All Public Works Continued:
Hazard Communication Program including training program(s)
  Steps to an Effective Hazard Communication Program for Employers That Use Hazardous Chemicals (osha.gov)
Confined Spaces – all Confined Spaces and Permit Required Confined Spaces
  Confined Spaces - Overview | Occupational Safety and Health Administration (osha.gov)
Respiratory Protection (if you require employee to wear a respirator
  https://www.osha.gov/respiratory-protection

## Slide 17: All Public Works Continued:
Control of Hazardous Energy (Lockout/Tagout)
  Control of Hazardous Energy (Lockout/Tagout) - Overview | Occupational Safety and Health Administration (osha.gov)
PPE Hazard Assessment
  Microsoft Word - PPE Assessment.doc (osha.gov)
Work Zone Safety – Manual on Uniform Traffic Control Devices
  Highway Work Zones and Signs, Signals, and Barricades - Overview | Occupational Safety and Health Administration (osha.gov)

## Slide 18: Over 1,500 Pounds of Chlorine Gas
Process Safety Plan and Program
  Process Safety Management for Storage Facilities (osha.gov)

## Slide 19: Illinois OSHA On-Site Consultation Program
Free and Confidential Safety and Health Advise
  Provides Recommendations to improve workplace safety and health
    1-800-972-4216
    IL On-Site Safety and Health Consultation Program - Consultation (illinois.gov)

## Slide 20: Clean Air Act 112(r) Risk Management Plans and Programs
Applies to water systems that store 2,500 pounds or more chlorine gas.
  Protects individuals, the general public, environment and infrastructure
NOT THE SAME AS OSHA PSM
Purpose of Rule:
Prevent accidental releases
Mitigate release consequences
Inform the public and government

## Slide 21: PROGRAM LEVEL 3
Management System
Hazard Assessment
Prevention Program
Emergency Response Requirements

## Slide 22: Written Management Plan
Document who is responsible
  Delineate individual with overall responsibility
  Describe roles and responsibilities of others

## Slide 23
Hazard Assessment
Document who is responsible
  Describe worst-case scenario for release
  Describe an alternate scenario (more likely than worst case)
  Describe mitigation system – stuff designed to minimize exposure
    Passive mitigation (only thing considered in worst case) – e.g., enclosed spaces
    Active mitigation - e.g., interlocks, shutdown systems, emergency isolation systems, gas scrubbers
  Describe 5-Year Accident History Criteria
    Consequences – On or Off-site injuries or deaths, evacuations, property damage, etc.
    Hold Public Meeting within 90 days of an accident with off-site impacts

## Slide 24: Prevention Program
Process Safety Information
  Best Management Practices (Recognized and Generally Accepted Good Engineering Practices)
  Chemical Hazards/Process Technology/Process Equipment
Process Hazard Analysis
  Identify potential hazards of potential for release
  Consider Operating Pressures/Human Error/Typical Causes of Accidents/Need for Mitigation
  Findings used to develop operating procedures
Operating Procedures
  Initial Startup/Normal Operations/Temporary Operations/Emergency Shutdown/Normal Shutdown/Re-Start Following Emergency and Normal Shutdown

## Slide 25: Prevention Program Continued
Training
  40 CFR 68
  Operating Procedures/Mechanical Integrity/Management of Change and Pre-Startup/Contractors/Emergency Response
Mechanical Integrity (Scales, detectors, piping, scrubbers, cranes, hoists)
  Critical to Safe Operations
  Prevents releases
  Saves Money
Compliance Audit
  Every three years
  Must be done by at least one person knowledgeable in water treatment (someone from the facility)

## Slide 26: Other Prevention Program Requirements
Incident Investigation
Management of Change
Pre-Startup Review
Employee Participation
Hot Work
Contractors
Emergency Response

## Slide 27: Illinois EPA Permit Requirements
To reduce the risk of chlorine gas release water systems must have gas scrubbers
Water System in existence before 2019 do not have to install scrubbers until major treatment renovation occurs or until upgrading chlorine storage/treatment unit(s)

## Slide 28: 35 IL Adm Code Part 604
Section 604.1115 Chlorine Gas
  Chlorinators that are housed separately from the chlorine storage must be in an adjacent room.
  Chlorinator rooms must be heated to 60 degrees Fahrenheit, and be protected from excessive heat. Cylinders and gas lines must be protected from excessive temperatures.
  Chlorine gas feed and storage must be enclosed and separated from other operating areas. Both the feed and storage rooms must be constructed so as to meet the following requirements:
    ….
      11) provisions must be made to chemically neutralize chlorine gas in the event of any measured chlorine release. The equipment must be sized to treat the entire contents of the largest storage container on site.

## Slide 29: 35 IL Adm Code Part 604 Continued
Section 604.145 Exceptions for Community Water Supplies
  A community water supply operating before July 26, 2019 is not required to modify or replace components to meet the requirements of this Part if:
    1) the requirements of 35 Ill. Adm. Code 611 are met;
    2) the requirements of Sections 604.205, 604.230 and 604.1210 are met;
    3) water pressure meets the standards of Section 604.1415(a)(1); and
    4) the components were permitted or no permits were required at the time of construction.

## Slide 30: 35 IL Adm Code Part 604 Continued
Section 604.160 Safety
  All community water supplies whose treatment involves chemical application must have and maintain a chemical safety plan.
  b) All community water supply personnel involved in the use and maintenance of chemicals must have periodic safety training.

## Slide 31: Review
Water Systems that use chlorine gas need to comply with EPRA
CWSs that store more than 1,500 pounds of chlorine gas need to take additional measures to consider worker safety and comply with OSHA Process Safety Management
If you build a new plant and want to use chlorine gas you will need to install a scrubber
CWSs that store more than 2,500 pounds of chlorine gas need to consider off-site releases and comply with U.S. EPA Risk Management
All Public Works Departments must consider worker safety

## Slide 32: Thank you